## Slide 1: Comfort Control

## Slide 2: Team Members
Wesley Swink
Team Lead Thermostat hardware design-Lead Vent design
Drew Fountain
Vent design-Lead Thermostat hardware design Temperature probe design

## Slide 3: Team Members
Jordan Freeman
Programming-Lead User interface Mobile application design
Nathan Wang
Mobile application design-Lead Programming Website design-Lead

## Slide 4: Faculty Advisor
Dr. Randy Follet
Ph.D., Electrical Engineering, Mississippi State University, 1988
M.S., Electrical Engineering, Mississippi State University, 1984
B.S., Electrical Engineering, Mississippi State University, 1982
Academic/Research and Fields of Interest:
System Simulation
Digital Control Systems
Sonar Signal Processing
Computer-Aided Control Systems Analysis and Design
Research/Organization Affiliations:
Eta Kappa Nu Electrical Engineering Honorary Society (HKN)

## Slide 5: Agenda
Problem
Solution
Constraints
  Technical
  Practical
Approach
Progress
Timeline
Questions

## Slide 6: What is the Problem?
Inconsistent and undesired temperatures throughout the household
No personalization
Manual vents

## Slide 7: Solution
Personalized comfort in every room
Automated Vents
On-the-go control

## Slide 8: Constraints

## Slide 9: Technical Constraints
Name | Description
Range | Thermostat hub must maintain WiFi connection with router up to 100 feet away
Air Flow | Vents must open by at least 0.5 inches to allow for adequate airflow
Integration | Thermostat hub must operate with existing thermostat connections
Size | System must monitor and control the climate of at least ten devices
Accuracy | Temperature sensors must be +/- 1 ℉ accurate

## Slide 10: Practical Constraints
Economic
  Comfort Control basic package $200
  Less than $100 for additional vent and thermometer probe

## Slide 11: Practical constraints
Social
  Mobile device application
  Easy-to-use interface
  Powerful control
Comfort Control
Master Bedroom
Currently 72° F
No schedules set.
Master Bedroom
Currently 72° F
No schedules set.
72
Living Room
Currently 68° F
Schedules: - 1:00pm – 5:00pm: 73
- 5:00pm – 9:30pm: 68
- 9:30pm – 3:00am: 70
68

## Slide 12: Approach

## Slide 13: Thermostat Hub Microcontroller (Constraint: Must monitor and control at least ten devices)
Component | Pros | Cons
Raspberry Pi Zero | Cheap Small Large dev community | No analog pins
BeagleBone Black | Analog pins | Large Expensive
Arduino Zero | Analog pins Large dev community | Expensive
Notes: https://www.adafruit.com/product/2885
Will run the GUI Communicate with mobile app
Retrieve room temps
Directly control vent servos

## Slide 14: Touchscreen
3.5” Display
480 x 320 resolution
Max current of 100mA
Notes: https://www.adafruit.com/product/2097

## Slide 15: Temperature Probe Microprocessor
Component | Pros | Cons
ESP8266 | Onboard WiFi Lowest Price Arduino Compatible | Few GPIO pins
Arduino Micro | Several GPIO pins | Most expensive ($24.95) No onboard WiFi
Adafruit Trinket | Arduino compatible | No onboard WiFi
Notes: https://www.seeedstudio.com/WiFi-Serial-Transceiver-Module-w-ESP8266-p-2485.html?ref=newInBazaar
Build into thermometer probe to communicate room temperature to thermostat over WiFi

## Slide 16: Temperature Sensor (Constraint: Must be +/- 1℉ accurate)
Component | Pros | Cons
DS18B20 | Digital Can connect directly to Raspberry Pi Single connection +/- 1℉ | Larger
Thermistor | Small Single connection +/- .2℉ | Analog Cannot connect directly to Raspberry Pi
MCP9808 | Wide voltage range +/- .5℉ | Most expensive Most connections

## Slide 17: Integration

## Slide 18: DC-DC Converter
Component | Pros | Cons
SMAKN LM2596 DC-DC Converter | Max input voltage Price High load current | Large
DROK LM2596 Numerical Control DC-DC Converter | Price LED display | Largest footprint Input voltage
TRACO Power TSR-1-2450 | Fixed 5v output Small footprint | Lowest load current Price

## Slide 19: Relay Module
Component | Pros | Cons
JBtek 4 Channel Relay | 4 relays Least expensive Highly recommended Extensive libraries | Requires extra circuit
Crydom CN240A05 (single) | Directly controlled by Pi Low current draw | Only one relay Bulky
Uxcell Solid State Relay (single) | Directly controlled by Pi Low current draw | Only one relay Bulky Most expensive

## Slide 20: Progress
Parts selected and purchased
Mobile application design
GUI design
Hardware testing
  Relay
  Servo
  Raspberry PI
Vent design

## Slide 21: Mobile Application Design
Overall Goal
  Generic user interface
  Intuitive and simple
  Log in screen
  Communication with thermostat
Currently
  Formatting temperature control screen
Comfort Control
Master Bedroom
Currently 72° F
No schedules set.
72
Living Room
Currently 68° F
Schedules: - 1:00pm – 5:00pm: 73
- 5:00pm – 9:30pm: 68
- 9:30pm – 3:00am: 70
68
Goal GUI
Current GUI
Notes: http://www.instructables.com/id/ESP8266-WiFi-DB18B20-temperature-sensor-ESP8266-Ar/?ALLSTEPS

## Slide 22: GUI Design
Basic framework
Window navigation
Functioning buttons
Current GUI >
< Goal GUI

## Slide 23: Hardware Testing
Successfully controlled solid state relay with Raspberry Pi
Successfully connected and controlled servo motor with Raspberry Pi

## Slide 24: Timeline
August
Begin researching
September
Begin selecting parts
Start on application and thermostat GUI and front end
Finalize vent and temperature probe design
Begin testing parts
October
Start on application and thermostat backend
Create physical vent and temperature probe prototypes
November
Integrate all parts of system
Begin system testing

## Slide 25: References
[1] Amazon.com, "SMAKN LM2596 DC-DC Buck Converter", 2016. [Online]. Available:
https://images-na.ssl-images-amazon.com/images/I/71gQyHR8llL._SL1500_.jpg [Accessed: September 16, 2016]
[2] Amazon.com, "JBtek 4 Channel 5V DC Relay Module", 2016. [Online]. Available:
https://images-na.ssl-images-amazon.com/images/I/712o-J5AgcL._SL1100_.jpg [Accessed: September 16, 2016]
[3] Adafruit.com, "Raspberry Pi Zero - Version 1.3" [Online]. Available:
https://www.adafruit.com/product/2885
[4] Adafruit.com, "PiTFT - Assembled 480x320 3.5" TFT+Touchscreen for Raspberry Pi", 2016. [Online]. Available:
https://www.adafruit.com/products/2097
[5] seeedstudio.com. "WiFi Serial Transceiver Module w& ESP8266", 2016. [Online]. Available:
https://www.seeedstudio.com/WiFi-Serial-Transceiver-Module-w-ESP8266-p-1994.html
[6] sparkfun.com. "One Wire Digital Temperature Sensor - DS18B20", 2016. [Online]. Available:
https://www.sparkfun.com/products/245

## Slide 26: Questions